Wildlife Watering Facilities - Guzzlers

A wildlife watering facility may be a guzzler, spring development, pond, wetland, or other type of water supply. This Technical Note provides specifications for guzzlers.

General guidelines:

Guzzler is a term used to describe self-filling, constructed watering facilities that collect, store, and make water available for wildlife.

Supplemental water is generally not a limiting factor for native Colorado upland wildlife species. Refer to Wildlife Species Models (WSMs) to determine whether adding water to a site will remove or improve a limiting factor. The planner and client may decide to add wildlife water for reasons other than removing a limiting factor. In cases where limiting factors are not addressed, upland wildlife habitat management (645) will not be reported.

The major components of guzzlers are a rain and snow collecting apron made of concrete, rubber, plastic, metal, or treated soil; a storage tank; and an escape ramp. A float system or a trough may also be needed depending on the design. An escape ramp is required in all watering facilities.

The following technical information will help determine spacing and volume needed in wildlife watering facilities for the targeted animals.

Site Selection:

1) A guzzler should be placed outside gullies, arroyos, or draws to avoid flood damage and siltation and should be protected from sunlight as much as possible. Orienting the tank so that the open end faces north helps keep water temperatures down and will minimize evaporation if no shade is available.  South facing slopes are preferable to north facing slopes to help with thawing in the winter.

2) For all watering facilities, a nearby food supply is critical for use by the selected wildlife species.

3) Other critical habitat components may be satisfied by planting a shrub thicket adjacent to the watering facility. Thickets provide escape, forage, and loafing cover for a number of birds, enhancing the habitat value of the facility. Some shrubs that provide these values include Skunkbush sumac, American plum, Rocky Mountain juniper, Gambel oak, Chokecherry, Buffaloberry, Winterfat, Four-wing saltbush, and Big sagebrush. Refer to ecological site indices to select appropriate shrub species for a given site.

Spacing:

Spacing of watering facilities is based on estimated distances wildlife will travel to water. The following distances are suggested spacings for watering facilities (Hoffman, et.al. 1993, Rintamaki 1986, SCS 1973, Schmidt 1996).

Species			Optimum (Miles)		Maximum (Miles)

Pronghorn antelope 		2				3-4

Mule deer			0.5				1

Elk				0.5				1

Chukar				0.5				1

Most quail species		0.5				1

Pheasant			0.5				1

Turkey				1				2

Mourning dove		3				5

All guzzler designs must be approved by someone with adequate delegated job approval authority.  The following information may be helpful in determining size of apron and storage needed.

Typical Wildlife Water Use Chart (Schmidt, 1996):

Pronghorn antelope 		1-2 gal/animal/day

Mule deer 			1-2 gal/animal/day

Elk 				5-8 gal/animal/day

Chukar 			750 gal/covey/year

Most quail species 		750 gal/covey/year

Wild Turkey 			7 gal/100head/day

Pheasant 			2-5 gal/flock/day (year round)

Mourning dove 		2-5 gal/flock/day (year round)

Efficiency and life spans of apron materials are (Kie et.al. 1996):

Steel - 98%, 25 years

Asphalt roofing - 86-92%, 8 years

Plastic covered with 1 inch of gravel - 66-87%, 8-15 years

Butyl rubber - 98%, 15-20 years

Asphalt paving - 95%, 15 years

Water storage needs are calculated using the low number in the average annual precipitation range along with the expected number of animals and their water needs. Colorado precipitation maps are available at: ftp://ftp.ftw.nrcs.usda.gov/pub/ams/prism/maps/co.pdf

The tank should be sized to hold enough water for the target species for one year. The apron should be sized to fill the storage tank once each year (assuming 100% water harvest). Potential yield of the apron surface can be calculated using the following formula based on the lowest average annual precipitation amounts. For example, if you are located in the 14-16 inch precipitation zone, you would use 14 inches as your expected precipitation amount.

Gallons needed x 12

Apron size (sq. ft.)  =  ----------------------------------------------------------------------

Average minimum precipitation x 7.48 x Efficiency

Example: A small flock of pheasants (20 birds) uses 2 gallons of water per day or 730 gallons/year (2 gallons/day x 365 days/year = 730 gallons/year).  In this example, we are located in a 12-14" precipitation zone, so we use 12” as our average minimum precipitation. We want to use a round apron on a prefabricated guzzler.  Plug these numbers into the above equation and the result is (730 gallons x 12) /(12 x 7.48 x 0.98) = 100 sq. ft. (apron size).  For a round apron, this equates to an 11.3 ft. diameter apron. The closest size in prefabricated guzzlers is 12 feet in diameter so you would select the 12 feet diameter, round guzzler design that will hold at least 730 gallons of water.  The tables at the end of this document provide common design sizes.

Additional Requirements, Concerns, and Considerations:

All guzzlers will be filled after installation and during prolonged dry periods.

Consider whether the purpose for installing guzzlers is to attract wildlife or to remove a limiting factor for the target species.  A guzzler may concentrate wildlife in one spot, creating the potential for predation and disease.

Use fencing to control livestock access to the guzzler. If a water development is for both livestock and wildlife, consider developing and fencing out a separate wildlife watering area.

Compensation for leakage and evaporation will require upward adjustments of component sizes and should be considered in the water budget.

Consider the effect this practice will have on water quantity (especially depletions) and advise the landowner to take necessary steps to get permits or water rights needed.

Existing water supplies may be adapted for wildlife following the above guidance. For example, water from a stock pond or a spring development could be used to develop a wildlife watering facility adjacent to the pond.

References:

Hoffman, R.W., H.G. Shaw, M.A. Rumble, B.F. Wakeling, C.M. Mollohan, S.D. Schemnitz, R. Engel-Wilson, D.A. Hengel. 1993. Management guidelines for Merriam's wild turkeys. Colorado Division of Wildlife Report #18. 24 pp.

Kie, J.G., V.C. Bleich, A.L. Medina, J.D. Yoakum, and J.W. Thomas. 1996. Managing rangelands for wildlife. Chapter 27 in Research and Management Techniques for Wildlife and Habitats, Ed. T.A, Bookhout. Pub. The Wildlife Society. 740 pp.

Rintamaki, R. 1986. Wyoming Biology Technical Notes #105(Elk), #110 (Mule deer), #114 (Pronghorn), #216 (Mourning dove), #220 (Sage grouse).

Soil Conservation Service (SCS) 1973. Management guide for turkey. 2pp.

Schmidt, R. 1996. Wildlife Watering Facility Standard and Specification. Nevada Field Office Technical Guide. 24 pp.

Snyder, W.D. 1969. A modified gallinaceous guzzler for scaled quail. Colorado Game, Fish, and Parks Outdoor Facts publication #65. 2 pp.

Spence, Ed. 1997. Personal communication on practical aspects of guzzler installation.

Yoakum, J. and W.P. Dasmann. 1971. Habitat Manipulation Practices. Chapter 14 in Wildlife Management Techniques, Third Edition. Ed. Robert H. Giles, Jr. Pub. The Wildlife Society. 633 pp.