## Interim HGM Model for Low Gradient Riverine Wetlands

### March 2000

Interim  Functional Assessment Model for Low Gradient (<2% channel slope) fine substrate (coarse sand or finer or embedded coarse substrate) riverine wetlands of Colorado, Montana, and Wyoming.  Rosgen (1996) channel types C5, C6, D5, D6, E5, E6, F5, F6, G5, and G6.

This subclass of riverine wetlands is found on the floodplain of  types C and E streams and their degraded states, types D, F, and G streams (Rosgen 1996).  These streams have a gradient of less than or equal to 2%.  The major water source is from overbank flow.  Secondary water sources include surface run-off from uplands and hyperiac connections between the stream and the wetlands.

These wetlands function as surface water storage and particulate retention areas.  The areas also provide important wildlife habitat components and nutrient cycling.

SUMMARY OF MODEL VARIABLE DEFINITIONS, MEASURES, AND METHODS.

Ventren: Rosgen’s entrenchment ratio (1996), width of the flood prone area (an elevation twice the maximum bank full depth) divided by the channel width at bank full.  Entrenchment ratio indicates access to the flood plain.  A high entrenchment ratio (>2) is indicative of good floodplain access.  An entrenchment ratio of 1 indicates no access to a floodplain.

METHODS: 1. Measure the bankfull width of the stream and the maximum bank full depth of the stream.  Multiply the maximum bank full depth by 2, stretch a tape at 2 times bank full depth above the channel bottom using a line level.  This is the elevation of the flood prone width.  Measure this width and divide by the bank full channel width.  This is the entrenchment ratio.

Compare channel condition to illustrations (Rosgen, 1996) and assign the value.

Note that Rosgen (1996) does not list entrenchment ratios for type D streams.  When working with type D streams, the entrenchment ratio would be greater than 2.2, thus you should use an index value of 1.0.

Vretar:  A roughness factor indicating resistance to flow.

METHODS: 1. Review retardance classes for dominant site conditions.  Select the condition that most closely matches the assessment area.

Vhymod: Watershed modification of hydrologic flow.  Significant alteration of the hydrograph, flood duration, magnitude, and frequency, by dams, flow augmentation, land management and other activities.  Regardless of entrenchment ratio, the frequency, duration, and magnitude of flooding can be altered by these activities.

METHODS: On-site observation coupled with use of photos for off-site modifications impacting the site.  Also consult with landowners for local information.

Vgeomod: Geomorphic modifications to the floodplain such as dikes and levees that limit floodplain access.

METHODS: On-site observation coupled with photos for off-site modifications impacting the site.  Also, consult with landowners for local information.

Vtext: Soil texture and organic matter content in order to retain and release elements and compounds.

METHODS: Estimate soil properties in the upper 6-18 inches of the soil profile.  Estimate soil texture, percent clay, percent organic matter, and soil color value.  Compare findings to the condition column for this variable.  This variable should be estimated for the dominant soil in the wetland being assessed.  The user must consider the source of low chroma soil colors that may be caused by things other than organic matter.

Vcomp: Species composition of dominant wetland vegetation as related to species composition for similar sites as reported in the literature.  Literature sources include The Colorado Natural Heritage Program’s “Classification of  Riparian Vegetation” for the various river basins, ecological site indices, etc.

METHODS: Compare existing dominant wetland/riparian vegetation with that reported in the literature.  Compare with the condition column for this variable and record the appropriate score.

Vstrat: The number of vegetative strata (e.g. trees, shrubs, and herbaceous = 3 strata) present on the site compared to that recorded in the literature (see Vcomp for literature sources) for similar sites.

METHODS: Determine the number of vegetative strata present on the site by observation.  Compare the number of strata observed to the number presented in the literature for this type of site.  Literature sources are the same as above.  Compare the difference between the observed and potential number of strata with the condition column for this variable.  Record the appropriate score.

Vregen: Regeneration of dominant plant species listed in V-comp.  Regeneration puts the maintenance in maintain characteristic plant community.

METHODS: Look for evidence of regeneration (seedlings, shoots, multiple age classes) of the dominant plant species in V-comp.  Compare with the condition column for this variable.

Vupuse: Land use in the adjacent uplands as it impacts wetland habitat quality and sustainability.

METHODS: Observe land use in the adjacent uplands.  Determine the dominant, or most limiting land use and refer to the condition column for this variable.  Enter the appropriate score.

References:

Kittel, G., E.VanWie, M.Damm, R.Rondeau, S.Kettler, A.McMullen, and J.Sanderson. 1999. A Classification of Riparian Wetland Plant Associations of Colorado. Colorado Natural Heritage Program, Colorado State University, Fort Collins, CO 80523.

Rosgen, D. 1996. Applied River Morphology.  Printed Media Co., Minneapolis, MN. pp. 5-15 through 5-25.

- DYNAMIC SURFACE WATER STORAGE

- MAINTAIN CHARACTERISTIC BIOGEOCHEMICAL PROCESSES

# Model Variable				Condition		Index

Ventren: width of the flood prone		Ratio: >2.2		1.0

area (an elevation twice the

maximum bank full depth)

divided by the channel width at

bank full.

Definition: The ability of surface		Ratio: 1.4 – 2.2		0.5

water to reach the flood plain

at an appropriate frequency and

depth.

Logic: The entrenchment ratio		Ratio <1.4>1.1		0.25

is indicative of access to the flood

plain.  In the absence of flow

control, (e.g. dams) the higher

the entrenchment ratio the

better the access to the flood		Ratio: 1.0		0.1

plain.  Flood frequency,

duration, and depth of flow

will be appropriate for the

system.

- DYNAMIC SURFACE WATER STORAGE

3.0  MAINTAIN CHARACTERISTIC BIOGEOCHEMICAL PROCESSES

# Model Variable				Condition		Index

Vretar: Retardance Class			Vegetation 		1.0

averaging 30 inches

Definition: A roughness factor		height or higher

indicating resistance to flow. 		(Retardance Class A).

Logic: Retardance is a surrogate 		Vegetation 		0.75

measure of surface roughness		averaging 12-29 inches

supplied by vegetation which		height (Retardance

influences the rate of surface flow 		Class B).

through the wetland and thus the

rate and amount of sediment		Vegetation 		0.3

deposition.				averaging 6-11 inches

or fallow (Retardance

class C).

Smooth, unvegetated	0.1

cropland or <6 inches

height.

1.0  MAINTAIN DYNAMIC SURFACE WATER STORAGE

# Model Variable				Condition		Index

Vhymod: Watershed modification		No significant 		1.0

of hydrologic flow.			modification in the

hydrograph.

Definition: Significant alteration, 		Modification in river	0.75

of hydrograph, flood frequency,		discharge from land

duration and magnitude by watershed	management or actual

modification.				augmentation resulting

in increased hydrographic

peak or duration.

Logic: Watershed alterations such as dams	Modifications in 		0.5

that significantly alter the hydrograph,	watershed (e.g.

alter the frequency, duration, and 		dams or diversions) with

magnitude of wetland inundation.		control of flow resulting

in decreased hydrographic

peak reducing overbank

flooding.

Modifications in 		0.1

watershed with control

of flow resulting in rare

overbank flooding.

1.0  MAINTAIN DYNAMIC SURFACE WATER STORAGE

# Model Variable				Condition		Index

Vgeomod: Geomorphic modifications to	No geomorphic 		1.0

the floodplain.				modifications (e.g.

dikes, levees, rip-rap,

bridge approaches,

Definition: Modifications that limit		roadbeds, etc.) made

floodplain access.				to floodplain.

Logic: Modifications that limit floodplain	Few of above changes 	0.6

access reduce the frequency and 		to floodplain.

magnitude of flooding of wetlands.

Multiple changes to 	0.2

floodplain surface to

control flood energy

but still permitting flow

access to backwater

and paleo-channels.

Modifications result in 	0.0

hydrologic disconnection

between river and

floodplain.

3.0  MAINTAIN CHARACTERISTIC BIOGEOCHEMICAL PROCESSES

# Model Variable				Condition		Index

Vtext: Soil Texture			Soil is fine or very fine	1.0

Textured (C, SiC, SC %

DEFINITION: The texture and organic	with >40clay) and soil

matter content of soil to retain and 		organic matter levels are

release elements and compounds.		>5% (soil survey report or

estimate) or soil color

LOGIC: Soil properties of the upper	value is </= 3.

6 to 18 inches of the soil impact the

soil’s ability to retain and release		Soil is medium or 	0.75

elements and compounds.  (Texture is	moderately fine textured

averaged to a depth of 18 inches; 		(L, CL, SiCL, SiL with

organic matter is measured in the 		20 to 40% clay) and soil

upper 6 inches of the A horizon).		organic matter levels are

>4 to <5% or soil color

value is </= 3.

Soil is medium or 	0.5

moderately coarse

textured (VFSL, SiL, L,

FSL, SL, coSL with 20%

clay and soil organic matter

is >2 to <4% or soil color

value is >3 to <4.

Soil is coarse textured	0.1

(LS, LfS, LcoS, S, fS,

coS, vfS, LvfS, with

<10% clay) and soil

organic matter is </=2%

or soil color value is >/=5.

The substrate is a 	0.0

non-porous medium

(e.g. pavement)

2.0 MAINTAIN CHARACTERISTIC PLANT COMMUNITY

3.0 MAINTAIN CHARACTERISTIC BIOGEOCHEMICAL PROCESSES

# Model Variable				Condition		Index

Vcomp: Vegetative species composition.	75-100% of dominant	1.0

plant species are native

DEFINITION: Percent of dominant		as described in the

vegetation that is native as described	literature for the site.

in the literature.

50-74% of dominant 	0.75

LOGIC: The maintenance of the 		plant species are native

characteristic plant community		as described in the

requires a predominance of native,		literature for the site.

non-invasive plant species.

25-49% of dominant 	0.5

plant species are native

as described in the

literature for the site.

<25% of dominant plant	0.25

species are native as

described in the literature

for the site.

Paved or no vegetation	0.0

on soil surface

- MAINTAIN CHARACTERISTIC PLANT COMMUNITY

- MAINTAIN CHARACTERISTIC BIOGEOCHEMICAL PROCESSES

# Model Variable				Condition		Index

Vstrat: The number of strata present in	Appropriate number of	1.0

the vegetative community.			vegetative strata for the

site as described in the

Use the CNHP guides for the river basin	literature are present.

where you are working to determine

appropriate number of strata.		One stratum for the site 	0.5

is missing.

Definition: The presence of the number

of vegetative strata for the site as 		More than one stratum	0.1

described in the literature.			is missing.

Impervious surface	0.0

Logic: The presence of the correct 		or bare soil surface

number of vegetative strata indicates

that habitat functions and biogeochemical

functions are being maintained at characteristic

levels.

2.0  MAINTAIN CHARACTERISTIC PLANT COMMUNITY

# Model Variable				Condition		Index

Vregen: Regeneration of native plants	Regeneration of 3 or 	1.0

more species listed in

Vcomp.

Definition: Regeneration of native		Regeneration of 1 –2 	0.5

plant species either vegetatively		species listed in

or sexually.				Vcomp.

Logic: Regeneration of native plant		No regeneration of 	0.0

species constitutes maintenance of 		dominant species

the characteristic plant community.		listed in Vcomp.

2.0  MAINTAIN CHARACTERISTIC PLANT COMMUNITY

# Model Variable				Condition		Index

Vupuse: Upland land use			Properly managed	1.0

native vegetation.

Definition: Dominant land use or 		Native vegetation		0.75

condition of the upland watershed that	under season long

contributes to the wetland.			grazing with moderate

use.

Land use affects quality of wetland habitat 		OR

by contributing sediment and attached	Idle grassland cover.

nutrients. 					OR

Permanent hayland.

Over grazed, some bare	0.5

ground, low plant vigor.

OR

No-till small grain.

OR

Minimum till in a grass/

legume rotation.

Severely over-grazed, 	0.25

high amounts of bare

ground, low plant vigor,

and evidence of soil erosion.

OR

No-till row crop, minimum

till small grain.

Row crop or		0.1

conventional tillage

small grain.

Urban			0.0

FUNCTIONS:

- MAINTAIN DYNAMIC SURFACE WATER STORAGE

This function is described by the variables Ventren, Vhymod, Vgeomod, and Vretar.  The variables Ventren, Vhymod, and Vgeomod describe the degree of alteration to the frequency, duration, and magnitude of overbank flow.  Vretar describes the capacity of the floodplain vegetation and microtopography to retard overbank flows to allow infiltration and storage.

INDEX OF FUNCTION

FCI = [(Ventren x Vhymod x Vgeomod)1/3 x Vretar]1/2

- MAINTAIN CHARACTERISTIC PLANT COMMUNITY

This function is described by the variables Vcomp, Vstrat, Vregen, and Vupuse.  The variables Vcomp and Vstrat describe the composition of the vegetation relative to similar sites as noted in the literature.  Vregen concerns the regeneration of native plant species described in Vcomp.  Vupuse characterizes upland land use as it impacts the characteristic plant community.

INDEX OF FUNCTION

FCI = [Vcomp x (Vstrat + Vregen + Vupuse)/3]1/2

- MAINTAIN CHARACTERISTIC BIOGEOCHEMICAL PROCESSES

This function is described by the variables Vtext, Vcomp, Vstrat, Vretar, and the FCI for function #1, Dynamic Surface Water Storage.  Vtext describes the soil capacity for storage and release of elements and compounds.  Vcomp and Vstrat describe the plant community and serve as a surrogate as to whether or not elemental cycling and other functions are characteristic for the site.  Vretar describes retardance to flow on the floodplain, providing opportunity for the biogeochemical functions to take place.   The FCI for dynamic surface water storage describes opportunity for overbank flow that drives the system.

INDEX OF FUNCTION

# FCI = (FCI #1 + Vtext + Vcomp + Vstrat + Vretar)/5

#### FCI Worksheet

Fill in the values for all the following variables:

Existing	Planned

Existing	Planned	Mitigation 	Mitigation

Site		Site

Ventren			________	________	________	_________

Vhymod			________	________	________	_________

Vgeomod			________	________	________	_________

Vretar				________	________ 	________	_________

Vcomp				________	________	________	_________

Vstrat				________	________	________	_________

Vregen				________	________	________	_________

Vupuse			________	________	________	_________

Vtext				________	________	________	_________

Acres				________	________	________	_________

Calculate the FCI and the FCUs for the three functions:

#1. Dynamic Surface Water Storage

FCI = [(Ventren x Vhymod x Vgeomod)1/3 x Vretar]1/2

_____= [(______ x ______ x ________)1/3 x ______]1/2   EXISTING

_____= [(______ x ______ x ________)1/3 x ______]1/2   PLANNED

_____= [(______ x ______ x ________)1/3 x ______]1/2   EXISTING MITIGATION SITE

_____= [(______ x ______ x ________)1/3 x ______]1/2   PLANNED MITIGATION SITE

FCI x Acres = FCU

Existing FCU	_____ - Planned FCU ______ =  ______

Planned mitigation site FCU _____ - Existing mitigation site FCU ____ = ______

Note: Planned mitigation site FCUs minus existing mitigation site FCUs must be equal to or greater than existing FCUs minus planned FCUs.

#2. Maintain Characteristic Plant Community

FCI = [Vcomp x (Vstrat + Vregen + Vupuse)/3]1/2

_____= [______ x (______ + ________ + _______)/3]1/2 EXISTING

_____= [______ x (______ + ________ + _______)/3]1/2 PLANNED

_____= [______ x (______ + ________ + _______)/3]1/2 EXISTING MITIG. SITE

_____= [______ x (______ + ________ + _______)/3]1/2 PLANNED MITIG. SITE

FCI x Acres = FCU

Existing FCU	_____ - Planned FCU _____ = ______

Planned mitigation site FCU _____ - Existing mitigation site FCU ____ = ______

Note: Planned mitigation site FCUs minus existing mitigation site FCUs must be equal to or greater than existing FCUs minus planned FCUs.

#3. Maintain Characteristic Biogeochemical Processes

# FCI = (FCI #1 + Vtext + Vcomp + Vstrat + Vretar)/5

_____= (______ + ______ + _______ + ______ + ______)/5 EXISTING

_____= (______ + ______ + _______ + ______ + ______)/5 PLANNED

_____= (______ + ______ + _______ + ______ + ______)/5 EXISTING MITIG. SITE

_____= (______ + ______ + _______ + ______ + ______)/5 PLANNED MITIG. SITE

FCI x Acres = FCU

Existing FCU	_____ - Planned FCU _____ = ______

Planned mitigation site FCU _____ - Existing mitigation site FCU ____ = ______

Note: Planned mitigation site FCUs minus existing mitigation site FCUs must be equal to or greater than existing FCUs minus planned FCUs.