# Sprinkler Irrigation Design Summary Worksheet

| Project Owner’s Name & Address: |
| --- |
| Project Location |
| Field No: | Legal Description: ________, Section ________, T________ , R________ ; ____________________________ County, Colorado |
| Project Designer |
| Design Prepared By: | Representing: (name of agency, company, etc.) | Date: |

| Basic Soil Data |
| --- |
| Soil Series | % of Irrigated Area | Average Slope, (%) | Available Water Holding Capacity, AWC (in/ft depth) | Sprinkler Intake Rate, (in/hr) | Depth in feet to | ECe(ave) (mmhos/cm) |
|  |  |  | 0 – 1 | 1 – 2 | 2 - 3 | 3 – 4 | 4 – 5 |  | Inhibiting Layer | Water Table |  |

ECe(ave) = Average Soil Extract Electrical Conductivity, (mmhos/cm)

| Basic Crop Data |
| --- |
| Crop to be Irrigated | Acres | Root Zone Depth (ft) | Total AWC (in) | MAD (%) | Peak Daily ETc (in/day) | Net Irrigation Requirement (in / month) | ECe(ct) (mmhos/cm) |

MAD =Management Allowed Depletion

ECe(ct), is the threshold salinity, maximum mean root zone soil salinity at which yield reductions will not occur.

| Irrigation Water Data |
| --- |
| Source | Available Volume (Ac-ft/yr) | Average | Seasonal Low | Water Quality |
|  |  | Flow Rate (gpm) | Pressure (psi) | Flow Rate (gpm) | Pressure (psi) | pH | TDS (mg/l) | ECw (mmho/cm) | SAR |

Irrigation System Planning Data

| Type of System: |  |
| --- | --- |
| Total Area Irrigated, A, (acres): |  |
| Crop Evapotranspiration, ETc, (inches per day) |  | (Use peak ETc for the critical design period) |
| Actual Operating Time, T, (hours/day): |  | (T is not to exceed 22 hours/day) |
| Assumed Application Efficiency, Ea, (%): |  |
| Minimum System Capacity, Qu, (gpm/acre): |  |
| Design Flow Rate, Q = Qu x A, (gpm): |  | Available Flow Rate, (gpm): |  |

Sprinkler Line Data

| Pipe Description: |  | Inside Diameter, ID, (in): |  |
| --- | --- | --- | --- |
| Thickness, (in) |  | Length, (ft): |  | Number of Outlets: |  | Inlet Pressure, (psi) |  |
| Elev. Head, (ft) Up (-) Down (+) |  | ( 2.31 = |  | + Friction Loss, (psi) |  | =Actual Pressure Loss, (psi): |  |
| Is Allowable Pressure Loss < 20% of sprinkler design operating pressure, (psi)? |  |

Sprinkler Head Data           (for center pivots, show data for the last tower & attach nozzle package design)

| Make: |  | Model: |  | Nozzle Size, (inches): |  |
| --- | --- | --- | --- | --- | --- |
| Drop Length, (ft): |  | Nozzle Height, (ft) |  | Pressure Regulators? Y N | Pressure, (psi) |  |
| Discharge, (gpm): |  | Wetted Diameter, (ft): |  | Spacing, (ft): |  |
|  |  | Application Time, (hrs): |  | Application Rate, (in/hr): |  |
| Net Application Depth = Application Time x Application Rate x Efficiency, (inches) = |  |
| Heerman-Hein Coefficient of Uniformity, CU, as determined from: (field evaluation) (model simulation- e.g: CPED) (design assumption) |  |
| Estimated Runoff as % of Water Applied, detrmined from: (field evaluation) (model simulation- e.g.: CPNOZZLE) (design assumption) |  |

Other System Components

| Item | Location | Description |
| --- | --- | --- |
| Flow Measuring Device |  |  |
| Surge Control (valve, chamber) |  |  |
| Air-Vacuum Valves |  |  |
| Pressure Relief Valves |  |  |
| Waterline Check Valve |  |  |
| Injection Line Check Valve |  |  |
| Drain Facilities |  |  |
| Other |  |  |

Attach Supporting Documentation that includes:  (Check all that apply)

- Irrigation Water Management Plan, describing:

- Method for determining net annual water requirement and peak daily ETc;

- Method for determining irrigation frequency and application depth;

- Rationale for selected Management Allowed Deficit (MAD) leaching fraction; and

- Describe proposed use for fertigation/chemigation

- On -site Survey and Soil Investigation Field Notes, as required

- Well/Pump Performance Test Results & Water Quality Analysis Report (< 1 year old)

- Filter Selection & Design Computations if required

- Hydraulic Design Computations & vendor’s nozzle package design printout

- Simulation Model(s) Data

##### Construction Drawings, Specifications, Material List and Itemized Cost Estimate

Attach plan view(s), aerial photo(s), map(s), etc. as needed to identify and locate:

- Area Irrigated with Sprinklers
Include field boundaries, utilities, system layout & direction of move, & prevailing wind direction

- Site Specific Elevation Grid or Contours 
Include map scale, legend, north arrow & critical elevations, note high & low points on sprinkler line

- Irrigation Well(s) or other Water Source 
Indicate design capacity (gpm) and operating pressure (psi)

- Delivery Pipeline (from source to sprinkler line)

Indicate sizes, lengths, locations, material type, pressure ratings

- Sprinkler Line(s), Control Station & Filter Station(s) & Valves